Table S1. Brief specifications of the 12–row and 15-row RS

| Serial Number | Description or component | 12- row RS | 15- row RS |
| --- | --- | --- | --- |
| 1 | Type of implement | Tractor mounted (Three point hitch) | Tractor mounted (Three point hitch) |
| 2 | Power required (horse power) | 35 or above | 35 or above |
| 3 | Ground clearance of machine (cm) | 114 | 114 |
| 4 | Working width (cm) | 270 | 303 |
| 5 | Gear box | Bevel crown wheel and pinion | Bevel crown wheel and pinion |
| Strip Tillage Unit |
| 6 | Type of rotor drive | Chain drive | Chain drive |
| 7 | Number of blades | 4 | 4 |
| 8 | Type of blade | Knife | Knife |
| 9 | Number of flanges | 12 | 15 |
| Furrow openers |
| 10 | Number of tool bars and mounting on main frame | 4 ; Alternate on front and back bar of main frame | 3 ; Alternate on front and back bar of main frame |
| 11 | Number of furrow openers | 12 ; 3 on each tool bar | 15; 5 on the each tool bar |
| 12 | Type of furrow openers | *SR, ZTT, ZTDD | SR, ZTT, ZTDD |
| 13 | Number of crop dividers | 4 | 3 |
| 14 | Row spacing (cm) | 18 cm between 3 openers of tool bar and 32 cm between adjacent set of openers of adjacent tool bar | 18 cm between 5 openers of tool bar and 29 cm between adjacent set of openers of adjacent tool bar |
| 15 | Seed metering device | Fluted feed rollers | Fluted feed rollers |
| 16 | Fertiliser metering device | Fluted feed rollers | Fluted feed rollers |

* SR- strip till, ZTT-zero till tine, ZTDD-zero till double disc openers, RS-Relay Seeder