SUPPLEMENTAL DATA

to accompany

First evidence of a “Barrovian”- type metamorphic regime in the Ross orogen of the Byrd Glacier area, Central Transantarctic Mountains, Antarctica

by Talarico et al.

The 40Ar/39Ar measurements were performed on separated mineral samples in the Radiogenic Isotopes Laboratory at Ohio State University.  The general procedures have been described previously (see Foland et al. 1993 and references therein) except for the use of a new noble-gas mass analysis system, for which detailed procedures and configurations will be described separately.  Sized aliquots (typically, 1-4 mg for mica, 6-12 mg for amphibole) of mineral separates were irradiated in the 5C position of the McMaster Nuclear Reactor, McMaster University, for 61.1 hours.  They were subsequently heated incrementally to successively higher temperatures using a custom-built resistance-heating, high-vacuum and low-blank furnace.  The step heating was continuous with ramp times from one temperature to another of about 1 minute and with dwell times of about 30 minutes at each temperature.  These incremental-heating fractions were analyzed by static gas mass analysis with a MAP 215-50 mass spectrometer.  Corrections for interfering reactions producing Ar from K, Ca, and Cl were made using factors determined from salts irradiated at the same time.  The monitor used was an intralaboratory muscovite standard (“AL-1”) that has an 40Ar/39Ar age of 443.52 Ma; an uncertainty of ± 1% is assigned to this age in order to allow for uncertainties in the standards against which AL-1 was calibrated.  The age for this monitor was determined by simultaneous cross calibration with several monitors including the Fish Canyon Tuff biotite standard (FCT-3) with an age of 27.84 Ma.

References

Foland, K.A., Fleming, T. H., Heimann, A. & Elliot, D.H. 1993. Potassium-argon dating of fine-grained basalts with massive Ar loss: Application of the 40Ar/39Ar technique to plagioclase and glass from the Kirkpatrick Basalt, Antarctica. Chemical Geology, 107, 173-190.

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKA hornblende  Run #68B8  (J = 0.013407   wt. = 10.65mg)

900	63.53	5.292	52.96	15.92	21.64	0.05	32.85	0.010	0.958	459.5	±	36.2

950	27.61	8.408	14.41	2.058	23.14	0.17	83.09	0.036	0.616	487.6	±	8.3

1000	23.20	9.427	8.518	0.4623	22.91	1.98	98.33	0.061	0.551	483.3	±	1.3

1028	23.06	9.266	7.557	0.4205	22.80	4.96	98.51	0.069	0.561	481.3	±	2.3

1050	23.21	8.903	8.129	0.4013	23.05	6.87	98.91	0.064	0.584	485.8	±	2.1

1075	23.17	8.858	8.350	0.3808	23.09	6.90	99.24	0.062	0.587	486.5	±	1.7

1100	23.17	8.884	8.107	0.4003	23.02	8.36	98.91	0.064	0.585	485.2	±	1.6

1120	22.95	8.816	8.115	0.3812	22.85	10.37	99.14	0.064	0.590	482.2	±	1.6

1140	23.12	8.855	8.079	0.3792	23.03	10.75	99.17	0.064	0.587	485.4	±	1.6

1160	23.20	8.886	8.107	0.3900	23.08	9.93	99.05	0.064	0.585	486.4	±	1.6

1180	23.05	8.805	8.088	0.3959	22.90	8.74	98.95	0.064	0.590	483.1	±	1.5

1200	23.19	8.820	7.994	0.4070	23.00	7.64	98.78	0.065	0.589	485.0	±	1.9

1220	23.35	8.861	8.281	0.3972	23.22	6.64	99.02	0.063	0.587	488.9	±	1.9

1240	23.11	8.770	8.150	0.4001	22.95	5.84	98.91	0.064	0.593	484.0	±	2.0

1260	23.45	8.829	8.345	0.4375	23.21	5.07	98.53	0.062	0.589	488.8	±	2.2

1280	23.35	8.778	8.374	0.4793	22.99	3.03	98.00	0.062	0.592	484.6	±	1.2

1300	23.56	8.837	8.471	0.5024	23.13	1.07	97.77	0.061	0.588	487.3	±	1.9

1320	23.51	8.851	8.530	0.6147	22.76	0.50	96.37	0.061	0.587	480.5	±	3.1

1341	23.82	8.879	8.071	0.7223	22.70	0.31	94.93	0.064	0.586	479.4	±	4.5

1361	23.82	8.812	8.743	0.8569	22.37	0.24	93.48	0.059	0.590	473.2	±	5.7

1382	24.34	8.959	9.176	0.9568	22.65	0.19	92.57	0.057	0.580	478.3	±	6.9

1401	24.72	8.927	7.981	1.113	22.44	0.15	90.42	0.065	0.582	474.6	±	8.6

1420	25.70	8.964	6.982	1.280	22.84	0.13	88.55	0.075	0.580	481.9	±	10.4

1440	24.86	8.635	7.001	0.7419	23.59	0.10	94.54	0.074	0.603	495.7	±	11.7

Integrated	23.21	8.874	8.167	0.4184	23.01	100	98.71	0.064	0.586	485.0

Plateau:

950 - 1300°C	(98% of 39Ar)	485.1	±	1.4

Isotope Correlation:

900 - 1440°C	N = 24	MSWD = 2.6	intercept 40Ar/36Ar = 280 ± 24	484.9	±	1.2

__________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	F c	39Ar d	40Ar* e	K/Ca f	K/Cl g	Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKA hornblende  Run #68B9  (J = 0.013398   wt. = 6.13mg)

700	349.7	3.959	142.9	116.2	20.80	0.22	5.22	0.003	1.23	443.4	±	193.8

875	33.32	6.443	22.16	3.456	25.64	0.16	75.54	0.023	0.797	532.7	±	46.6

950	23.28	9.230	8.435	0.4911	22.99	4.94	98.11	0.062	0.562	484.4	±	1.9

1000	22.91	9.254	7.648	0.3578	22.93	38.32	99.52	0.068	0.561	483.4	±	1.6

1020	23.08	7.568	9.200	0.4777	22.84	4.24	98.30	0.056	0.685	481.7	±	1.6

1040	24.27	8.669	9.442	0.9017	22.85	1.01	93.46	0.055	0.598	481.8	±	4.1

1070	23.42	8.877	9.040	0.5584	22.98	2.74	97.44	0.057	0.584	484.2	±	2.9

1100	23.20	8.936	8.893	0.4674	23.02	3.39	98.53	0.058	0.580	484.9	±	2.2

1120	23.35	9.374	8.882	0.5070	23.06	3.52	98.10	0.058	0.553	485.8	±	2.3

1140	23.12	9.173	8.022	0.4129	23.01	7.21	98.94	0.065	0.566	484.8	±	1.8

1160	23.03	8.968	7.928	0.3727	23.02	6.16	99.39	0.066	0.579	485.0	±	1.8

1180	23.17	8.864	7.879	0.3666	23.17	9.50	99.44	0.066	0.586	487.8	±	1.6

1200	24.00	8.604	8.806	0.6800	23.17	1.17	95.89	0.059	0.603	487.8	±	3.5

1220	23.28	8.916	7.497	0.3919	23.17	2.69	99.00	0.069	0.583	487.8	±	2.7

1240	25.41	8.443	7.991	0.9950	23.56	0.46	92.16	0.065	0.615	494.9	±	8.6

1260	25.40	8.302	8.723	1.574	21.89	0.30	85.64	0.060	0.625	464.0	±	16.7

1280	23.12	8.620	7.817	0.4167	22.96	3.27	98.74	0.066	0.602	483.9	±	2.5

1300	26.65	8.255	8.501	1.485	23.40	0.25	87.23	0.061	0.629	491.9	±	11.0

1325	23.64	8.422	7.649	0.5660	23.02	1.04	96.82	0.068	0.617	484.9	±	6.6

1350	24.69	7.907	8.841	0.9648	22.99	0.22	92.51	0.059	0.656	484.4	±	17.3

1400	23.16	8.517	8.324	0.3920	23.12	8.52	99.23	0.062	0.609	486.9	±	1.6

1450	35.97	6.540	3.000	5.261	20.92	0.38	58.05	0.174	0.799	445.8	±	6.5

1500	55.27	6.081	6.544	12.56	19.00	0.18	34.19	0.079	0.858	409.1	±	25.8

1600	64.97	6.472	6.215	14.83	21.98	0.10	33.66	0.084	0.807	465.7	±	58.4

Integrated	24.03	8.942	8.347	0.7370	22.99	100	95.08	0.062	0.580	484.4

Plateau:

950 - 1300°C	(99% of 39Ar)	484.7	±	1.4

Isotope Correlation:

950 – 1240, 1280 – 1400 °C	N = 18	MSWD = 1.7	intercept 40Ar/36Ar = 297 ± 35	485.1	±	1.3

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JMZ biotite  Run #68B33  (J = 0.013114   wt. = 1.57mg)

500	13.97	0.1564	0.1636	0.8379	11.49	2.65	82.39	3.20	36.5	253.2	±	1.4

600	19.27	0.1601	0.0518	0.2290	18.57	5.78	96.54	10.1	35.3	393.2	±	0.9

625	22.50	0.1680	0.0320	0.1819	21.94	6.99	97.66	16.3	33.5	456.3	±	2.0

640	22.66	0.1654	0.0257	0.1883	22.08	6.62	97.59	20.3	34.1	458.9	±	2.5

650	22.95	0.1698	0.0285	0.0550	22.77	5.91	99.34	18.4	33.1	471.3	±	2.3

660	22.83	0.1694	0.0037	0.0109	22.78	5.67	99.90	141	33.1	471.5	±	1.1

670	23.25	0.1706	0.0403	0.1888	22.67	6.06	97.65	13.0	33.0	469.6	±	2.8

680	23.86	0.1712	0.0270	0.3805	22.71	6.41	95.33	19.4	32.9	470.4	±	2.3

690	23.31	0.1721	0.0260	0.2287	22.62	6.40	97.14	20.1	32.6	468.6	±	2.0

700	23.06	0.1701	0.0223	0.1478	22.61	6.41	98.15	23.5	33.0	468.4	±	1.8

710	23.02	0.1677	0.0061	0.0030	22.99	4.62	100.00	86.1	33.5	475.4	±	1.0

720	23.04	0.1685	0.0089	0.0151	22.97	3.70	99.85	58.5	33.3	475.0	±	1.0

730	23.10	0.1688	0.0151	0.0537	22.92	2.70	99.35	34.6	33.3	474.2	±	1.5

740	23.39	0.1683	0.0195	0.1461	22.94	1.51	98.19	26.8	33.4	474.4	±	1.8

750	24.37	0.1675	0.0369	0.5136	22.83	0.93	93.81	14.2	33.7	472.5	±	2.5

760	24.45	0.1718	0.0303	0.4759	23.02	0.74	94.28	17.3	32.8	475.9	±	3.3

770	24.45	0.1626	0.0347	0.7044	22.34	0.68	91.52	15.1	34.9	463.6	±	3.2

780	23.33	0.1654	0.0468	0.2792	22.49	0.66	96.51	11.2	34.1	466.3	±	3.5

790	23.21	0.1699	0.0401	0.2312	22.51	0.60	97.10	13.0	33.1	466.6	±	3.7

800	22.98	0.1657	0.0436	0.2741	22.16	0.59	96.52	12.0	34.0	460.2	±	3.7

830	23.19	0.1643	0.0441	0.1320	22.78	0.88	98.37	11.8	34.3	471.6	±	2.8

860	23.87	0.1743	0.0485	0.0868	23.60	1.14	98.98	10.8	32.2	486.5	±	2.6

890	24.58	0.1806	0.0403	0.0756	24.34	2.10	99.14	13.0	31.0	499.7	±	1.5

920	24.22	0.1805	0.0344	0.0453	24.07	3.68	99.50	15.2	31.0	494.9	±	1.2

950	23.82	0.1769	0.0342	0.0506	23.65	5.41	99.42	15.3	31.6	487.3	±	1.3

970	23.55	0.1750	0.0442	0.0532	23.38	4.54	99.38	11.8	32.0	482.4	±	1.0

990	23.68	0.1723	0.0720	0.0524	23.51	3.11	99.41	7.26	32.5	484.8	±	1.3

1010	23.55	0.1678	0.1354	0.1107	23.21	1.77	98.69	3.86	33.5	479.4	±	1.6

1030	23.46	0.1651	0.2509	0.1691	22.97	0.97	97.99	2.08	34.1	474.9	±	2.2

1050	23.24	0.1468	0.3909	0.3946	22.09	0.47	95.14	1.34	38.9	458.9	±	4.1

1075	21.17	0.1145	0.7302	0.6459	19.31	0.30	91.28	0.716	51.4	407.2	±	6.2

Integrated	22.81	0.1694	0.0414	0.1663	22.30	100	97.89	12.6	33.2	462.7

Plateau:

650 - 830°C	(55% of 39Ar)	“471.0	±	1.4”

________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JMZ biotite  Run #68B34  (J = 0.013109   wt. = 2.07mg)

550	13.38	0.1678	0.1679	0.8872	10.74	2.08	80.50	3.11	33.8	237.7	±	1.4

600	19.13	0.1695	0.0392	0.2106	18.48	8.39	96.79	13.4	33.2	391.4	±	1.7

625	22.65	0.1772	0.0019	0.0764	22.40	8.69	99.03	277	31.6	464.4	±	1.5

650	23.13	0.1796	0.0003	0.0424	22.98	9.98	99.49	1750	31.1	475.1	±	1.6

665	23.87	0.1774	0.0023	0.2773	23.02	8.79	96.59	227	31.6	475.8	±	1.8

680	22.76	0.1717	0.0010	0.0054	22.74	9.35	99.97	500	32.6	470.7	±	1.7

700	23.00	0.1761	0.0014	0.0712	22.76	6.13	99.11	384	31.8	471.1	±	2.0

720	22.41	0.1719	0.0001	0.0231	22.31	5.47	99.72	3150	32.6	462.9	±	2.5

740	22.96	0.1715	0.0023	0.0243	22.87	5.13	99.72	227	32.7	473.0	±	2.1

760	23.19	0.1766	0.0074	0.0060	23.15	3.05	99.96	71.0	31.7	478.1	±	1.3

780	23.14	0.1719	0.0141	0.0392	23.00	2.10	99.53	37.2	32.6	475.4	±	1.3

800	23.15	0.1730	0.0127	0.0254	23.06	1.46	99.71	41.0	32.4	476.4	±	1.5

820	23.19	0.1686	0.0183	0.0415	23.05	1.23	99.50	28.6	33.3	476.3	±	2.1

840	22.68	0.1713	0.0172	0.0511	22.51	1.09	99.37	30.3	32.7	466.5	±	2.5

860	23.53	0.1707	0.0313	0.0278	23.43	1.09	99.69	16.7	32.9	483.2	±	2.1

880	24.35	0.1824	0.0398	0.0416	24.21	1.35	99.54	13.2	30.6	497.2	±	2.1

910	24.42	0.1854	0.0377	0.0327	24.30	2.38	99.65	13.9	30.1	498.9	±	1.5

940	24.43	0.1841	0.0251	0.0665	24.21	5.03	99.23	20.9	30.3	497.3	±	2.0

970	23.68	0.1792	0.0261	0.0125	23.62	7.38	99.88	20.1	31.2	486.6	±	1.8

1000	23.67	0.1745	0.0496	0.0158	23.60	6.05	99.85	10.5	32.1	486.3	±	1.6

1030	23.83	0.1647	0.1806	0.0300	23.73	1.97	99.72	2.90	34.2	488.7	±	1.3

1060	23.32	0.1253	0.3896	0.0124	23.29	0.63	100.00	1.34	46.0	480.7	±	3.1

1090	20.76	0.0732	0.6419	0.2253	20.13	0.34	97.05	0.814	85.6	422.5	±	4.3

1120	18.95	0.0555	0.7057	0.2248	18.32	0.32	96.79	0.741	121	388.3	±	5.1

1150	21.47	0.0332	0.5752	0.3864	20.36	0.24	94.89	0.909	253	426.7	±	6.6

1200	25.19	0.0304	0.3020	0.3363	24.20	0.26	96.15	1.73	291	497.1	±	6.7

Integrated	22.71	0.1736	0.0292	0.0915	22.41	100	98.85	17.9	32.3	464.7

Plateau:

650 - 840°C	(54% of 39Ar)	“473.1	±	1.8”

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKL muscovite  Run #68B24  (J = 0.013210   wt. = 2.13mg)

500	9.531	0.0330	0.0014	0.7235	7.371	0.69	77.52	380	264	167.6	±	1.7

600	12.51	0.0169	0.0038	0.0755	12.71	0.63	99.79	136	1010	280.0	±	1.5

620	15.48	0.0153	0.0055	0.0437	15.59	0.60	99.84	95.2	1480	337.8	±	1.6

640	16.82	0.0161	0.0040	0.0458	16.93	0.73	99.81	130	1190	364.1	±	1.6

680	18.01	0.0158	0.0067	0.0216	18.05	1.58	99.36	77.6	1320	385.8	±	1.0

680	19.34	0.0150	0.0040	0.0390	19.43	1.03	99.60	131	1600	412.2	±	1.2

700	20.46	0.0156	0.0093	0.1340	20.04	1.25	98.07	56.1	1480	423.7	±	1.3

720	22.77	0.0164	0.0118	0.6684	20.77	1.86	91.32	44.4	1580	437.5	±	1.4

740	21.86	0.0138	0.0080	0.1717	21.33	2.11	97.68	65.1	3110	447.8	±	1.0

760	21.68	0.0131	0.0148	0.0068	21.68	2.19	99.98	35.3	4040	454.4	±	0.9

780	21.99	0.0131	0.0180	0.0069	21.99	2.60	99.99	29.1	4270	460.0	±	0.9

800	21.82	0.0128	0.0235	0.0146	21.76	2.96	99.81	22.3	5860	455.8	±	0.9

820	22.05	0.0128	0.0304	0.0010	22.04	3.11	99.24	17.2	5220	460.9	±	1.3

840	22.17	0.0124	0.0332	0.0313	22.06	5.34	99.59	15.7	9780	461.4	±	1.5

860	22.10	0.0127	0.0268	0.0145	22.04	6.20	99.82	19.5	6450	461.0	±	1.4

880	22.25	0.0128	0.0155	0.0222	22.16	6.91	99.71	33.7	6030	463.3	±	1.5

900	22.19	0.0128	0.0200	0.0184	22.11	7.83	99.76	26.1	5650	462.3	±	1.3

910	22.31	0.0126	0.0103	0.0088	22.26	7.12	99.89	50.9	7000	465.0	±	1.1

925	22.17	0.0124	0.0081	0.0151	22.11	8.01	99.80	65.0	10100	462.2	±	1.3

930	22.14	0.0125	0.0150	0.0265	22.04	6.85	99.65	34.8	8370	461.0	±	1.4

940	22.36	0.0132	0.0095	0.0241	22.26	6.24	99.69	55.1	3850	465.1	±	1.4

950	22.38	0.0130	0.0102	0.0234	22.29	5.60	99.69	51.3	4640	465.6	±	1.6

960	22.33	0.0123	0.0093	0.0335	22.21	4.63	99.56	56.1	12100	464.1	±	1.9

970	22.25	0.0128	0.0056	0.0176	22.28	2.33	99.82	93.2	5340	465.4	±	1.2

980	22.25	0.0127	0.0073	0.0071	22.21	2.22	99.91	71.4	6210	464.1	±	0.8

990	22.24	0.0128	0.0029	0.0021	22.22	1.84	99.70	178	5740	464.4	±	1.0

1000	22.39	0.0128	0.0069	0.0030	22.38	1.65	99.50	75.8	5420	467.3	±	1.2

1020	22.24	0.0130	0.0107	0.0039	22.23	1.87	99.69	48.7	4600	464.5	±	1.0

1040	22.39	0.0131	0.0170	0.0028	22.38	1.83	99.50	30.8	4270	467.3	±	1.0

1060	22.31	0.0135	0.0400	0.0238	22.36	1.23	99.33	13.1	3090	466.9	±	1.3

1080	22.27	0.0149	0.0927	0.0000	22.26	0.62	99.03	5.64	1690	465.0	±	2.3

1100	21.95	0.0155	0.1360	0.0462	21.81	0.33	99.43	3.85	1460	456.7	±	2.5

Integrated	21.86	0.0132	0.0157	0.0339	21.74	100	99.55	33.2	4140	455.4

Plateau:

820 - 990°C	(74% of 39Ar)	463.1	±	1.3

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKL muscovite  Run #68B26  (J = 0.013187   wt. = 3.76mg)

500	8.874	0.0212	- - - - -	0.6656	6.886	0.78	77.79	- - - - -	641	156.8	±	1.2

600	13.65	0.0152	- - - - -	0.1034	13.32	1.41	97.76	- - - - -	1640	291.9	±	0.9

620	17.37	0.0158	- - - - -	0.0575	17.18	1.06	99.02	- - - - -	1370	368.4	±	1.1

640	18.48	0.0157	- - - - -	0.0525	18.31	1.33	99.16	- - - - -	1390	390.1	±	1.0

680	19.77	0.0153	- - - - -	0.1116	19.42	2.80	98.34	- - - - -	1590	411.3	±	0.7

680	20.49	0.0143	- - - - -	0.0235	20.40	1.67	99.68	- - - - -	2150	429.8	±	0.9

700	21.40	0.0154	- - - - -	0.1211	21.02	1.94	98.34	- - - - -	1590	441.5	±	0.9

720	21.38	0.0137	- - - - -	0.0106	21.32	2.60	99.86	- - - - -	2800	447.0	±	0.8

740	21.72	0.0150	- - - - -	0.0062	21.68	2.73	99.92	- - - - -	1650	453.6	±	1.8

760	22.18	0.0138	- - - - -	0.0399	22.04	3.51	99.47	- - - - -	2820	460.2	±	1.8

780	22.23	0.0136	- - - - -	0.0189	22.16	4.03	99.76	- - - - -	3020	462.4	±	1.3

800	22.06	0.0139	- - - - -	0.0141	22.00	4.54	99.81	- - - - -	2630	459.5	±	1.5

820	22.14	0.0131	- - - - -	0.0127	22.08	5.23	99.83	- - - - -	4280	461.0	±	1.6

840	22.13	0.0134	- - - - -	-0.0018	22.12	5.91	100.03	- - - - -	3460	461.7	±	1.3

860	22.30	0.0137	- - - - -	0.0130	22.24	8.08	99.84	- - - - -	2820	463.9	±	1.1

880	22.21	0.0138	- - - - -	0.0200	22.13	9.13	99.75	- - - - -	2740	462.0	±	1.0

895	22.29	0.0134	- - - - -	0.0078	22.24	10.04	99.90	- - - - -	3350	464.0	±	1.2

910	22.44	0.0136	- - - - -	0.0107	22.39	9.46	99.86	- - - - -	3050	466.7	±	1.1

920	22.26	0.0135	- - - - -	-0.0094	22.26	6.26	100.13	- - - - -	3180	464.4	±	1.1

930	22.21	0.0141	- - - - -	0.0247	22.12	3.78	99.67	- - - - -	2330	461.7	±	1.3

940	22.56	0.0153	- - - - -	0.0039	22.52	2.41	99.95	- - - - -	1530	469.2	±	1.8

950	22.42	0.0124	- - - - -	0.0320	22.30	1.77	99.58	- - - - -	10300	465.1	±	1.2

960	22.37	0.0136	- - - - -	0.0517	22.19	1.45	99.32	- - - - -	3210	463.1	±	1.1

970	22.50	0.0132	- - - - -	0.0382	22.36	1.31	99.50	- - - - -	4150	466.2	±	1.0

980	22.51	0.0131	- - - - -	0.0790	22.25	1.07	98.96	- - - - -	4560	464.2	±	1.2

990	22.52	0.0133	- - - - -	0.0523	22.35	0.93	99.32	- - - - -	3960	466.0	±	1.4

1000	22.59	0.0138	- - - - -	0.1132	22.23	0.73	98.52	- - - - -	3070	463.9	±	1.5

1020	22.61	0.0143	- - - - -	0.1312	22.20	0.63	98.29	- - - - -	2390	463.2	±	1.7

1040	22.76	0.0143	- - - - -	0.1382	22.33	0.46	98.22	- - - - -	2340	465.7	±	1.9

1060	22.55	0.0138	- - - - -	0.1327	22.13	0.36	98.27	- - - - -	3050	462.0	±	2.2

1080	22.63	0.0124	- - - - -	0.1571	22.14	0.28	97.95	- - - - -	23900	462.1	±	3.0

1100	22.76	0.0135	- - - - -	0.1624	22.26	0.25	97.89	- - - - -	3750	464.3	±	3.0

1130	23.12	0.0139	- - - - -	0.2121	22.47	0.29	97.29	- - - - -	3180	468.2	±	3.1

1200	22.88	0.0145	- - - - -	0.1713	22.35	0.56	97.79	- - - - -	2240	466.1	±	1.9

1300	23.01	0.0138	- - - - -	0.2157	22.36	1.16	97.24	- - - - -	3320	466.1	±	1.4

1400	38.79	0.0345	- - - - -	5.980	21.08	0.02	54.38	- - - - -	456	442.5	±	5.5

Integrated	21.82	0.0139	- - - - -	0.0350	21.69	100	99.53	- - - - -	2640	453.9

Plateau:

760 - 1200°C	(84% of 39Ar)	“463.4	±	1.3”

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKL biotite  Run #68B20  (J = 0.013247   wt. = 3.87mg)

500	257.1	0.1883	- - - - -	81.27	16.96	0.58	6.60	- - - - -	220	365.6	±	75.5

600	43.08	0.0374	- - - - -	7.459	21.02	1.94	48.81	- - - - -	452	443.1	±	6.4

620	35.16	0.0304	- - - - -	4.523	21.78	4.07	61.97	- - - - -	517	457.3	±	3.5

640	29.88	0.0271	- - - - -	2.658	22.00	6.61	73.70	- - - - -	509	461.4	±	2.5

650	27.26	0.0254	- - - - -	1.755	22.06	6.73	80.97	- - - - -	510	462.5	±	1.8

660	25.29	0.0237	- - - - -	1.048	22.17	7.33	87.74	- - - - -	527	464.5	±	1.6

670	23.81	0.0228	- - - - -	0.6128	21.98	7.51	92.39	- - - - -	533	460.9	±	1.4

680	22.91	0.0225	- - - - -	0.3418	21.88	8.08	95.59	- - - - -	523	459.1	±	1.4

700	22.60	0.0224	- - - - -	0.1963	22.00	9.53	97.44	- - - - -	514	461.4	±	1.2

720	22.21	0.0221	- - - - -	0.0918	21.92	9.92	98.78	- - - - -	519	459.9	±	1.2

740	22.35	0.0218	- - - - -	0.0507	22.18	7.97	99.34	- - - - -	528	464.8	±	1.0

760	22.34	0.0227	- - - - -	0.0200	22.26	4.71	99.74	- - - - -	483	466.3	±	1.5

780	22.34	0.0223	- - - - -	0.1049	22.01	2.27	98.62	- - - - -	510	461.6	±	1.8

800	22.39	0.0218	- - - - -	0.1047	22.06	1.32	98.62	- - - - -	538	462.5	±	1.2

825	22.21	0.0223	- - - - -	0.1092	21.86	1.34	98.55	- - - - -	510	458.9	±	1.2

850	22.36	0.0225	- - - - -	0.1223	21.98	1.09	98.40	- - - - -	501	461.0	±	1.3

880	22.42	0.0222	- - - - -	0.1406	21.98	0.85	98.15	- - - - -	517	461.0	±	1.3

915	22.56	0.0221	- - - - -	0.1426	22.12	1.80	98.14	- - - - -	522	463.6	±	1.2

960	22.43	0.0218	- - - - -	0.1385	22.00	4.42	98.18	- - - - -	539	461.4	±	1.6

1000	22.62	0.0219	- - - - -	0.1302	22.22	5.24	98.30	- - - - -	530	465.4	±	1.5

1040	22.59	0.0226	- - - - -	0.1042	22.26	4.18	98.64	- - - - -	495	466.2	±	1.4

1080	22.76	0.0217	- - - - -	0.1647	22.25	1.78	97.86	- - - - -	547	466.0	±	1.1

1130	23.40	0.0246	- - - - -	0.3334	22.40	0.57	95.80	- - - - -	430	468.7	±	1.6

1200	24.96	0.0267	- - - - -	0.6566	23.00	0.17	92.22	- - - - -	382	479.8	±	3.6

Integrated	25.90	0.0245	- - - - -	1.313	22.00	100	85.01	- - - - -	512	461.4

Plateau:

620 - 960°C	(86% of 39Ar)	“461.7	±	1.3”

Isotope Correlation:

500 – 1130°C	N = 23	MSWD = 4.2	intercept 40Ar/36Ar = 288 ± 7	463.2	±	1.2

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JKL biotite  Run #68B21  (J = 0.013236   wt. = 2.71mg)

500	26.65	0.0467	0.0101	2.340	19.71	0.49	74.03	51.6	172	418.2	±	3.2

600	20.71	0.0259	0.0006	0.2721	19.88	0.81	96.11	849.7	386	421.5	±	1.3

620	21.78	0.0228	0.0000	0.1307	21.37	1.67	98.23	2610.0	488	449.3	±	1.1

640	21.93	0.0224	0.0003	0.1032	21.60	4.69	98.61	1930.0	505	453.7	±	1.5

650	22.01	0.0216	0.0841	0.0633	21.80	5.87	99.18	6.2	540	457.4	±	1.2

660	22.06	0.0213	0.0062	0.0453	21.90	7.97	99.39	83.9	556	459.2	±	1.1

670	21.88	0.0213	0.0000	0.0102	21.83	6.27	99.86	2610.0	553	457.9	±	1.3

680	22.06	0.0213	0.0009	0.0442	21.90	6.89	99.41	562.9	555	459.3	±	1.1

700	22.65	0.0226	-0.0001	0.2616	21.85	6.95	96.58	578.9	507	458.3	±	1.4

720	22.06	0.0210	0.0000	0.0560	21.87	7.90	99.25	2610.0	577	458.7	±	1.1

740	22.01	0.0208	0.0000	0.0248	21.92	8.01	99.67	2610.0	583	459.5	±	1.2

760	22.21	0.0222	0.0012	0.0833	21.95	6.08	98.89	433.4	513	460.1	±	1.3

780	22.36	0.0220	0.0002	0.1461	21.90	3.79	98.07	272.6	527	459.3	±	1.5

800	22.45	0.0220	0.0051	0.2112	21.81	1.30	97.22	103.5	532	457.5	±	0.9

825	22.58	0.0219	0.0169	0.1467	22.13	1.19	98.09	30.9	532	463.4	±	1.3

850	21.90	0.0226	0.0216	0.0390	21.76	0.81	99.48	24.2	489	456.7	±	1.7

880	21.89	0.0224	0.0287	0.0122	21.83	0.79	99.85	18.2	494	457.9	±	1.5

915	21.91	0.0225	0.0243	0.0390	21.77	0.95	99.48	21.5	491	456.8	±	1.5

960	21.92	0.0219	0.0127	0.0333	21.80	1.71	99.56	41.1	522	457.3	±	0.9

1000	22.25	0.0213	0.0037	0.0613	22.05	4.55	99.19	142.9	561	462.0	±	1.8

1040	22.07	0.0228	0.0003	0.0282	21.97	6.79	99.62	186.5	479	460.4	±	1.3

1080	22.29	0.0213	0.0039	0.0121	22.23	7.62	99.84	134	556	465.3	±	1.4

1130	22.28	0.0214	0.0041	0.0224	22.19	5.87	99.70	126	549	464.7	±	1.3

1200	22.30	0.0212	0.0112	-0.0061	22.30	0.86	100.09	46.5	558	466.6	±	1.5

1300	22.25	0.0242	0.0124	0.0934	21.95	0.19	98.76	42.0	427	460.1	±	2.8

Integrated	22.15	0.0218	0.0066	0.0798	21.89	100	98.94	79.8	530	459.1

Plateau:

660 - 1040°C	(72% of 39Ar)	“459.3	±	1.2”

__________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JNG muscovite  Run #68B44  (J = 0.013018   wt. = 3.36mg)

500	9.990	0.0566	- - - - -	0.3249	9.007	1.29	90.44	- - - - -	118	200.0	±	1.0

600	16.54	0.0534	- - - - -	0.5051	15.02	1.26	91.00	- - - - -	129	322.2	±	1.2

630	16.60	0.0659	- - - - -	0.0568	16.41	1.76	99.04	- - - - -	96.7	349.2	±	0.9

660	18.26	0.0672	- - - - -	0.0543	18.08	2.37	99.17	- - - - -	94.6	381.3	±	0.9

680	21.43	0.0598	- - - - -	0.5760	19.70	2.57	92.08	- - - - -	111	411.9	±	1.0

700	20.97	0.0452	- - - - -	0.0652	20.76	2.67	99.11	- - - - -	157	431.5	±	1.1

720	21.44	0.0358	- - - - -	0.0111	21.38	3.43	99.87	- - - - -	218	443.1	±	1.5

740	21.90	0.0298	- - - - -	0.0107	21.91	4.12	99.17	- - - - -	290	452.7	±	1.7

760	22.02	0.0269	- - - - -	0.0151	21.95	4.52	99.82	- - - - -	348	453.4	±	1.4

780	22.09	0.0243	- - - - -	0.0190	22.01	5.64	99.76	- - - - -	420	454.6	±	1.6

800	22.31	0.0230	- - - - -	0.0086	22.26	6.53	99.90	- - - - -	469	459.1	±	1.5

820	22.24	0.0217	- - - - -	0.0110	22.18	7.86	99.87	- - - - -	530	457.7	±	1.5

840	22.70	0.0217	- - - - -	0.0073	22.65	7.42	99.92	- - - - -	529	466.1	±	1.2

860	22.70	0.0214	- - - - -	0.0232	22.61	7.75	99.71	- - - - -	549	465.4	±	1.4

880	22.53	0.0215	- - - - -	0.0097	22.48	8.41	99.89	- - - - -	543	463.0	±	1.4

900	22.57	0.0215	- - - - -	0.0093	22.52	8.02	99.89	- - - - -	540	463.8	±	1.1

910	22.67	0.0217	- - - - -	0.0301	22.56	5.64	99.62	- - - - -	534	464.5	±	1.4

920	22.68	0.0228	- - - - -	0.0221	22.59	4.33	99.73	- - - - -	478	465.1	±	1.3

930	22.62	0.0249	- - - - -	0.0447	22.47	3.27	99.43	- - - - -	403	462.8	±	2.0

936	22.56	0.0238	- - - - -	0.0215	22.47	2.22	99.73	- - - - -	439	462.9	±	0.9

950	22.52	0.0245	- - - - -	0.0364	22.39	1.94	99.54	- - - - -	416	461.4	±	1.4

960	22.51	0.0246	- - - - -	0.0308	22.40	1.64	99.61	- - - - -	412	461.5	±	1.5

970	22.55	0.0250	- - - - -	0.0319	22.43	1.30	99.60	- - - - -	400	462.2	±	1.2

980	22.62	0.0253	- - - - -	0.0384	22.48	1.05	99.51	- - - - -	390	463.1	±	1.4

990	22.40	0.0251	- - - - -	0.0550	22.21	0.80	99.29	- - - - -	397	458.3	±	1.7

1000	22.46	0.0269	- - - - -	0.0467	22.30	0.65	99.40	- - - - -	349	459.8	±	1.8

1025	22.45	0.0302	- - - - -	0.0506	22.27	0.56	99.35	- - - - -	285	459.3	±	2.0

1050	22.59	0.0313	- - - - -	0.0691	22.36	0.43	99.12	- - - - -	270	460.9	±	2.5

1075	22.79	0.0326	- - - - -	0.1704	22.26	0.28	97.81	- - - - -	256	459.2	±	3.0

1100	23.12	0.0339	- - - - -	0.0118	23.06	0.27	99.87	- - - - -	237	473.6	±	3.7

Integrated	21.92	0.0278	- - - - -	0.0449	21.76	100	99.41	- - - - -	328	449.9

Plateau:

840 - 980°C	(53% of 39Ar)	464.1	±	1.3

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JNG muscovite  Run #68B45  (J = 0.013007   wt. = 2.62mg)

500	9.512	0.0556	0.0266	0.3232	8.530	0.83	89.96	19.6	121	189.8	±	1.2

600	14.00	0.0514	0.0277	0.0183	13.92	0.73	99.64	18.9	132	300.1	±	1.1

630	16.00	0.0640	0.0255	0.0236	15.90	1.02	99.59	20.5	100	339.2	±	1.0

660	17.04	0.0706	0.0241	0.0309	16.92	1.47	99.49	21.7	88.9	358.8	±	1.0

680	18.95	0.0670	0.0243	0.0570	18.75	1.56	99.13	21.5	94.8	393.8	±	0.9

700	21.33	0.0589	0.0264	0.4944	19.84	1.61	93.16	19.8	113	414.2	±	1.1

720	20.77	0.0455	0.0303	0.0274	20.66	1.85	99.63	17.3	155	429.5	±	1.0

740	21.39	0.0367	0.0360	0.0114	21.33	2.29	99.86	14.5	210	441.8	±	0.9

760	21.91	0.0313	0.0404	0.0198	21.83	4.20	99.75	13.0	269	450.8	±	1.6

780	22.20	0.0279	0.0417	0.0410	22.05	5.33	99.47	12.6	327	455.0	±	1.4

800	22.29	0.0257	0.0351	0.0116	22.23	7.45	99.86	14.9	377	458.2	±	1.3

820	22.42	0.0225	0.0282	0.0352	22.28	9.49	99.55	18.6	492	459.2	±	0.9

840	22.64	0.0222	0.0291	0.0567	22.44	6.47	99.27	18.0	510	462.0	±	1.3

860	22.46	0.0206	0.0275	0.0047	22.42	6.36	99.95	19.0	597	461.7	±	1.3

880	22.54	0.0203	0.0217	0.0217	22.45	6.59	99.72	24.1	622	462.1	±	1.1

900	22.53	0.0201	0.0149	0.0134	22.46	7.35	99.83	35.1	633	462.5	±	1.3

910	22.37	0.0203	0.0150	0.0142	22.30	6.23	99.82	34.8	617	459.4	±	1.4

920	22.67	0.0207	0.0133	0.0131	22.60	5.39	99.84	39.2	589	465.0	±	1.6

930	22.54	0.0205	0.0169	0.0402	22.39	4.82	99.48	30.9	606	461.1	±	1.3

940	22.74	0.0204	0.0147	0.0404	22.59	4.27	99.48	35.5	614	464.8	±	1.9

950	22.47	0.0208	0.0141	0.0080	22.41	2.29	99.90	37.1	584	461.5	±	0.8

960	22.48	0.0216	0.0182	0.0170	22.40	1.90	99.78	28.8	538	461.4	±	1.0

970	22.39	0.0225	0.0180	0.0142	22.32	1.71	99.82	29.0	493	459.8	±	1.1

980	22.47	0.0236	0.0245	0.0094	22.41	1.47	99.89	21.3	446	461.5	±	1.4

990	22.59	0.0245	0.0267	0.0278	22.48	1.30	99.65	19.6	415	462.8	±	1.5

1000	22.46	0.0257	0.0285	0.0441	22.30	1.13	99.43	18.3	380	459.4	±	1.5

1025	22.37	0.0273	0.0370	0.0175	22.30	1.23	99.78	14.1	338	459.4	±	1.4

1050	22.23	0.0277	0.0469	0.0185	22.15	1.26	99.77	11.2	330	456.7	±	1.1

1075	22.36	0.0311	0.0697	0.0319	22.24	0.98	99.61	7.50	272	458.4	±	1.2

1100	22.12	0.0333	0.1251	0.0702	21.89	0.62	99.11	4.18	244	452.1	±	1.8

1150	23.18	0.0381	0.3173	0.1516	22.73	0.37	98.18	1.65	201	467.2	±	2.5

1225	23.21	0.0293	0.4026	0.1033	22.91	0.42	98.82	1.30	302	470.5	±	2.4

Integrated	22.01	0.0266	0.0291	0.0359	21.87	100	99.53	18.0	357	451.7

Plateau:

840 - 1025°C	(59% of 39Ar)	462.0	±	1.3

__________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JNG biotite  Run #68B40  (J = 0.013063   wt. = 1.84mg)

500	26.30	0.3016	0.0337	1.762	21.08	6.75	80.22	15.5	18.2	438.8	±	3.7

650	22.54	0.2989	0.0069	0.2441	21.81	35.45	96.83	75.4	18.2	452.2	±	0.9

675	22.66	0.3023	0.0017	0.0603	22.47	12.82	99.25	301	18.0	464.3	±	1.5

720	22.84	0.3069	0.0092	0.1007	22.53	11.37	98.73	56.8	17.7	465.4	±	1.3

740	22.47	0.3071	0.0047	0.0259	22.38	4.75	99.69	110	17.7	462.7	±	1.1

760	22.23	0.2972	0.0094	0.0120	22.18	2.51	99.88	55.7	18.3	459.1	±	1.3

780	22.23	0.2815	0.0147	0.0053	22.22	1.79	99.74	35.5	19.4	459.7	±	1.5

800	22.44	0.2799	0.0214	0.0415	22.31	1.70	99.49	24.4	19.5	461.4	±	1.8

820	23.97	0.2852	0.0228	0.5907	22.21	1.50	92.75	22.9	19.2	459.7	±	1.8

840	22.33	0.2827	0.0232	0.0681	22.11	1.66	99.14	22.6	19.3	457.8	±	1.5

860	22.41	0.2794	0.0181	0.0147	22.35	1.84	99.84	28.8	19.5	462.1	±	1.5

880	22.21	0.2805	0.0075	0.0106	22.16	2.30	99.89	69.6	19.4	458.7	±	1.4

900	22.34	0.2906	0.0055	0.0273	22.25	2.97	99.67	95.2	18.7	460.3	±	1.3

920	22.34	0.2956	0.0050	0.0442	22.20	3.38	99.45	105	18.4	459.3	±	1.3

940	22.24	0.2964	0.0039	0.0644	22.04	3.16	99.18	136	18.4	456.5	±	1.4

960	22.30	0.3031	0.0052	0.0638	22.09	2.36	99.19	101	17.9	457.4	±	1.6

980	22.57	0.3088	0.0098	0.0830	22.32	1.65	98.95	53.4	17.6	461.5	±	1.6

1000	22.80	0.3093	0.0119	0.1315	22.40	1.10	98.33	43.9	17.6	463.0	±	2.1

1020	23.26	0.2997	0.0288	0.1280	22.87	0.55	98.41	18.1	18.1	471.7	±	3.3

1060	23.86	0.3423	0.3305	0.3745	22.77	0.25	95.50	1.58	15.8	469.8	±	6.1

1080	25.58	0.3039	0.2177	0.5067	24.09	0.12	94.24	2.40	17.9	493.6	±	10.2

Integrated	22.82	0.2989	0.0104	0.2484	22.07	100	96.82	50.1	18.2	457.1

Plateau:

675 - 1000°C	(57% of 39Ar)	“462.0	±	1.4”

_________________________________________________________________________________________________

40Ar/39Ar analytical results:

__________________________________________________________________________________________________

T a	40Ar b	38Ar b	37Ar b	36Ar b	 F c	 39Ar d	 40Ar* e	 K/Ca f	 K/Cl g	 Apparent

____  	____  	____  	____

39Ar	39Ar	39Ar	39Ar	(%)	(%)	Age h  (Ma)

(x100)

__________________________________________________________________________________________________

JNG biotite  Run #68B42  (J = 0.013040   wt. = 2.26mg)

500	67.29	0.3229	0.0646	15.49	21.52	1.81	31.99	8.10	18.5	446.2	±	9.5

600	23.31	0.2971	0.0040	0.8884	20.67	3.28	88.79	132	18.4	430.5	±	1.1

620	24.22	0.3006	0.0208	0.7260	22.06	7.12	91.20	25.1	18.2	456.1	±	2.1

630	22.91	0.2956	0.0124	0.3626	21.82	8.55	95.38	42.3	18.4	451.7	±	1.5

640	22.62	0.2995	0.0193	0.1479	22.16	9.58	98.14	27.1	18.2	458.0	±	1.6

650	22.41	0.2977	0.0153	0.1220	22.03	10.48	98.46	34.2	18.3	455.6	±	1.4

660	22.44	0.2988	0.0045	0.0859	22.17	10.79	98.94	116	18.2	458.1	±	1.4

670	22.32	0.2980	0.0126	0.0836	22.05	9.77	98.96	41.4	18.3	456.0	±	1.5

680	23.09	0.3049	0.0233	0.1853	22.53	8.02	97.70	22.5	17.8	464.6	±	1.6

690	22.91	0.3035	0.0243	0.2611	22.13	4.61	96.70	21.5	17.9	457.3	±	2.1

700	22.75	0.3075	0.0016	0.1137	22.40	3.18	98.59	320	17.7	462.3	±	1.0

710	22.45	0.3100	0.0109	0.0479	22.30	2.60	99.44	47.9	17.5	460.5	±	1.2

720	22.14	0.3074	0.0170	0.0733	21.91	1.51	99.10	30.8	17.7	453.3	±	1.3

730	23.11	0.2994	0.0232	0.3547	22.05	0.79	95.53	22.6	18.2	455.9	±	2.0

740	25.08	0.2971	0.0242	1.012	22.07	0.49	88.13	21.6	18.4	456.4	±	3.0

760	22.18	0.2843	0.0424	0.0275	22.08	0.60	99.71	12.3	19.2	456.5	±	2.6

780	22.09	0.2807	0.0318	0.1343	21.68	0.78	98.28	16.4	19.4	449.2	±	2.1

800	22.21	0.2859	0.0427	0.0278	22.11	0.97	99.71	12.3	19.1	457.1	±	1.8

820	22.17	0.2821	0.0341	0.0738	21.94	1.07	99.09	15.3	19.3	453.9	±	1.7

840	22.33	0.2789	0.0329	0.0590	22.14	1.32	99.29	15.9	19.6	457.6	±	1.5

860	22.31	0.2820	0.0232	0.0383	22.18	1.67	99.56	22.5	19.3	458.4	±	1.3

880	22.33	0.2857	0.0130	0.0656	22.13	2.03	99.20	40.4	19.1	457.3	±	1.2

900	22.24	0.2883	0.0070	0.0343	22.12	2.55	99.61	74.6	18.9	457.2	±	1.1

925	22.41	0.2955	0.0097	0.0808	22.16	2.54	99.00	54.0	18.4	457.9	±	1.1

950	22.50	0.3039	0.0086	0.1134	22.15	1.84	98.58	60.7	17.9	457.7	±	1.2

975	22.67	0.3057	0.0207	0.1842	22.12	1.23	97.67	25.3	17.8	457.1	±	1.5

1000	22.45	0.2958	0.0436	0.0936	22.16	0.62	98.85	12.0	18.4	458.0	±	2.3

1025	23.18	0.2836	0.1387	0.5549	21.54	0.18	93.03	3.77	19.3	446.6	±	5.7

Integrated	23.53	0.2987	0.0166	0.4905	22.06	100	93.90	31.5	18.3	456.2

Plateau:

660 - 1000°C	(59% of 39Ar)	“458.4	±	1.4”

__________________________________________________________________________________________________

Notes to data table

_____________________________________________________________________________________________

a  Temperature in °C measured with a thermocouple on the outside of the Ta crucible.

b  The isotope ratios given are not corrected for Ca, K and Cl derived Ar isotopic interference but, 37Ar is corrected for decay using a half-life of 35.1 days.  The ratios are corrected for line blanks.

c  F is the ratio of radiogenic 40Ar to K-derived 39Ar.  It is corrected for atmospheric argon and other nuclear reactions using the following factors:

(38Ar/39Ar)K	=	0.0126504

(38Ar/37Ar)Ca	=	0.0000350

(39Ar/37Ar)Ca	=	0.0006796

(36Ar/37Ar)Ca	=	0.0002703

(40Ar/39Ar)K	=	0.0307767

(40Ar/36Ar)air	=	295.5

(36Ar/38Ar)Cl	=	2.018  10-6 per day after irradiation.

d  Relative percent of the total 39Ar released in the fraction.

e  Percent of the total 40Ar in the fraction that is radiogenic.

f  Weight ratio calculated using the relationship: K/Ca = 0.523  (39ArK/37ArCa).

g  Weight ratio calculated using the relationship: K/Cl = 5.220  (39ArK/38ArCl).

h  Ages calculated with a total decay constant of 5.543  10-10 y-1.  For increments of a step-heating analysis, the uncertainties do not include J value uncertainty.  For total-fusion, plateau and other ages, uncertainties reflect a relative uncertainty of ± 0.25% in J value.  A plateau is defined as contiguous fractions constituting more than 50% of the 39Ar released where the apparent-age variations among fractions may be accounted for with analytical uncertainties.  A plateau encompasses as many fractions as possible (except where fraction uncertainties are very large) where ages agree with the plateau within ± their two-sigma uncertainties.  Where this strict definition is not observed and variation among "plateau" fractions is minor but still exceeds analytical uncertainties, an approximate plateau is defined; in these cases, the indicated "plateau" age is enclosed in quotation marks.  An overall systematic uncertainty of ±1% is assigned to all ages.  The monitor used was a intralaboratory biotite standard (“AL-1”) that has a 40Ar/39Ar age of 443.5 Ma; an uncertainty of ± 1% is assigned to this age in order to allow for uncertainties in the standards against which AL-1 was calibrated.  The age for this monitor was determined by simultaneous cross calibration with several monitors including the Fish Canyon Tuff biotite standard (FCT-3) with an age of 27.84 Ma.

____________________________________________________________________________________________