# Supplementary material

Figure S1. Errors in TDDFT excitation energies computed using the B3LYP functional for charge-transfer transitions of molecules reported by Peach et al. in Ref. 8 as well as for dye WS-2 in vacuum For WS-2, the experimental absorption peak maximum is taken from ref. 5.

Table S1. HOMO and LUMO levels of the three dyes with all computational schemes considered in the paper.

| SIESTA (vacuum) |
| --- |
| eV | WS-2 | WS-2.1 | WS-2.2 | WS-2.1-WS-2 | WS-2.2-WS-2 |
| HOMO | -4.590 | -4.567 | -4.441 | 0.023 | 0.149 |
| LUMO | -3.416 | -3.494 | -3.466 | -0.078 | -0.050 |
| Mean HOMO | -4.581 | -4.543 | -4.444 | 0.037 | 0.137 |
| Mean LUMO | -3.481 | -3.552 | -3.495 | -0.072 | -0.014 |
| Gaussia 09, HOMO and LUMO in a.u., change vs. WS-2 in eV |
| vacuum B3LYP |
|  | WS-2 | WS-2.1 | WS-2.2 | WS-2.1-WS-2 | WS-2.2-WS-2 |
| HOMO, eV | -0.19529 | -0.19469 | -0.19262 | 0.0163268377 | 0.0726544277 |
| LUMO, eV | -0.12711 | -0.12772 | -0.12486 | -0.0165989516 | 0.0612256413 |
| vacuum CAM-B3LYP |
|  | WS-2 | WS-2.1 | WS-2.2 | WS-2.1-WS-2 | WS-2.2-WS-2 |
| HOMO, eV | -0.23628 | -0.23531 | -0.23116 | 0.0263950542 | 0.1393223482 |
| LUMO, eV | -0.09409 | -0.09661 | -0.09497 | -0.0685727183 | -0.0239460286 |
| MeCN B3LYP |
|  | WS-2 | WS-2.1 | WS-2.2 | WS-2.1-WS-2 | WS-2.2-WS-2 |
| HOMO, eV | -0.19296 | -0.19409 | -0.19351 | -0.0307488776 | -0.0149662679 |
| LUMO, eV | -0.12953 | -0.13204 | -0.13277 | -0.0683006043 | -0.0881649235 |
| MeCN CAM-B3LYP |
|  | WS-2 | WS-2.1 | WS-2.2 | WS-2.1-WS-2 | WS-2.2-WS-2 |
| HOMO, eV | -0.23462 | -0.23502 | -0.23073 | -0.0108845585 | 0.105852331 |
| LUMO, eV | -0.0964 | -0.10077 | -0.10407 | -0.1189138011 | -0.2087114083 |

Details of electronic structure calculations

The structures of the three molecules were optimized in vacuum and in MeCN (modelled as polarized continuum model, PCM) in Gaussian 09  using DFT with the B3LYP functional and visible spectra and oscillator strengths computed using TDDFT and the B3LYP (hybrid) and CAM-B3LYP (range-separeted) functionals. The LANL2DZ basis was used. The strongest and lowest energy transition in all dyes is due to HOMO-LUMO transition, to the tune of more than 85%. We therefore focus on this transition.

Details of molecular dynamics simulations.

Simulations were performed in SIESTA using DFT and the PBE functional in a simulation box of size 30 x 20 x 14 A. The standard DZP basis set was used with the EnergyShift parameter reduced to 0.01 Ry from the default value. Core electrons were treated with Troullier-Martins pseudopotentials provided with SIESTA.  The Brillouin zone was sampled at the  point. Prior to MD calculations, geometries were optimized until the forces on all atoms were below 0.02 eV/A. Nove-Hoover thermostat with the constant of 10.0 Ry*fs2 was used. The time step was 1 fs. The trajectories were run for 20 ps at 300K to thoroughly sample all molecular vibrations. First 3 ps were discarded for equilibration.